INSTRUCTIONS TO AUTHORISED FORKLIFT TRUCK DRIVERS:

- Write the date under the appropriate day of the week;

- Carry out the checks listed below; and

- If any defects are found, mark the appropriate box with an ‘X’, record the details of the defect(s) on the reverse of this sheet, and complete the action plan. You must also report the defect(s) to [Job role / Name] immediately.

IF THE FORKLIFT TRUCK IS FOUND TO BE DEFECTIVE IN ANY WAY THEN IT MUST NOT BE USED.

Week commencing (date): ______ / ______ / ___________

| All Trucks |
| --- |
|  | Mon | Tues | Weds | Thurs | Fri |
| Ref. | Check |
| 1 | Check previous defects have been corrected |  |  |  |  |  |
| 2 | Obvious leaks |  |  |  |  |  |
| 3 | Body work (any damage) |  |  |  |  |  |
| 4 | Lift rams / hydraulic pipes (any damage / debris / weaknesses) |  |  |  |  |  |
| 5 | Forks and latch pins (any damage, cracks) |  |  |  |  |  |
| 6 | Carriage and back plate |  |  |  |  |  |
| 7 | Mast / roller / slides (any damage or foreign items / appropriate lubrication) |  |  |  |  |  |
| 8 | Chains / pulleys / stop bolts / pins (any damage, obvious stretching, appropriate lubrication) |  |  |  |  |  |
| 9 | Condition of wheels (especially flanges on rims fitted with pneumatic tyres) |  |  |  |  |  |
| 10 | Tightness and security of wheel nuts |  |  |  |  |  |
| 11 | Condition of tyres (obvious damage) |  |  |  |  |  |
| 13 | Tyre pressure of pneumatic tyres |  |  |  |  |  |
| 16 | Hydraulic oil level (correct when forks are in parked position) |  |  |  |  |  |
| 17 | All hydraulic controls (including visual check for leaks) |  |  |  |  |  |
| 18 | Operating controls / system |  |  |  |  |  |
| 19 | Isolation switch operation |  |  |  |  |  |
| 20 | Lights / electric controls |  |  |  |  |  |
| 21 | Braking operations – hand / foot |  |  |  |  |  |
| 22 | Parking brake |  |  |  |  |  |
| 23 | Steering operations |  |  |  |  |  |
| 24 | Horn / seat / seat belt (correctly fitted and functioning correctly) |  |  |  |  |  |
| 25 | Functional test for lifting, tilting and manipulation |  |  |  |  |  |
| 26 | Functional test of attachments |  |  |  |  |  |
| 27 | Condition of overhead guard / load back-rest extension |  |  |  |  |  |
| 28 | Mirrors (plus any other visibility aids if fitted) |  |  |  |  |  |
| 29 | Gauge / Instruments |  |  |  |  |  |
| 30 | Alarms / other warning devices |  |  |  |  |  |
| 31 | Other checks |  |  |  |  |  |
| 32 | Other checks |  |  |  |  |  |

| Petrol / Diesel / LPG |
| --- |
|  | Mon | Tues | Weds | Thurs | Fri |
| Ref. | Check |
| 1 | Fuel level |  |  |  |  |  |
| 2 | Fuel connectors |  |  |  |  |  |
| 3 | Engine Oil Level |  |  |  |  |  |
| 4 | Engine |  |  |  |  |  |
| 5 | Coolant level |  |  |  |  |  |
| 6 | Battery |  |  |  |  |  |
| 7 | Fan / other belts |  |  |  |  |  |
| 8 | Inching pedal |  |  |  |  |  |
| 9 | LPG bottle security |  |  |  |  |  |
| 10 | Other checks |  |  |  |  |  |

| Electric |
| --- |
|  | Mon | Tues | Weds | Thurs | Fri |
| Ref. | Check |
| 1 | Electrolyte levels |  |  |  |  |  |
| 2 | Cable connections |  |  |  |  |  |
| 3 | Motor |  |  |  |  |  |
| 4 | Battery security |  |  |  |  |  |
| 5 | Battery charger (switched off, charge lead disconnected and stored properly) |  |  |  |  |  |
| 6 | Batteries (charged and leak free) |  |  |  |  |  |
| 7 | Other checks |  |  |  |  |  |

|  | Monday | Tuesday | Wednesday | Thursday | Friday |
| --- | --- | --- | --- | --- | --- |
| Date |  |  |  |  |  |
| Print Name |  |  |  |  |  |
| Signature |  |  |  |  |  |

DETAILS OF ANY DEFECTS MUST BE RECORDED ON THE REVERSE OF THIS SHEET

ACTION PLAN

| Date | Ref | Description of defect(s) | Action Required | Person Responsible | Target Date | Date Completed |
| --- | --- | --- | --- | --- | --- | --- |

# Text boxes

Disclaimer

These example forms, checklists and model policies are provided by Hettle Andrews for general guidance on matters of interest.  In making these documents available to a general and diverse audience it is not possible to anticipate the requirements or the hazards of any subscriber’s business.  Users are therefore advised to carefully evaluate the contents and adapt the forms and checklists to suit the requirements of each situation.  Hettle Andrews does not accept any liability whatsoever for injury, damage or other losses which may arise from reliance on this information and the use of these documents.

Copyright of these documents remains with Hettle Andrews and whilst subscribers are permitted to make use of them for their own purposes, permission is not granted for resale of the intellectual property to third parties.