Report form number:

Notes on testing to be undertaken in accordance with BSEN50172:2004/ BS5266-8:2004

Monthly

a) Simulate a failure of the supply to the normal lighting for a period sufficient to ensure that each lamp is illuminated either by using a key switch or by cutting power to the lighting circuit via the distribution board (if safe to do so). Check that all luminaries and signs are present, clean and functioning correctly.

b) Restore the supply and check that all indicators show that the normal supply has been restored.

c) For central battery systems, check the correct operation of system monitors.

Annually

In addition to the monthly checks, conduct a discharge test of the full rated duration according to the manufacturer’s information. All full duration tests should wherever possible be undertaken preceding time of low risk to allow for battery recharge.

| Date of system commissioning |  | Is a certificate of commissioning available? |  |
| --- | --- | --- | --- |
| Date of inspection/test |  |
| Location/zone |  |
| Details of inspector Note. If this is a member of staff write name and job title |  |
| Confirm outcome | All lamps operating correctly Defects identified as listed below |
| Defects identified |  |
| Action required |  |
| Action taken Note. include details of any alterations made to the emergency lighting system Date completed |  |

Signature of inspector/tester:

Name:

Position/qualification

Date:

# Text boxes

Page 1	                                                                                                                                         Hettle Andrews Form 2018

www.hettleandrews.co.uk

Disclaimer

These example forms, checklists and model policies are provided by Hettle Andrews for general guidance on matters of interest. In making these documents available to a general and diverse audience it is not possible to anticipate the requirements or the hazards of any subscriber’s business.  Users are therefore advised to carefully evaluate the contents and adapt the forms and checklists to suit the requirements of each situation. Hettle Andrews does not accept any liability whatsoever for injury, damage or other losses which may arise from reliance on this information and the use of these documents.

Copyright of these documents remains with Hettle Andrews and whilst subscribers are permitted to make use of them for their own purposes, permission is not granted for resale of the intellectual property to third parties.

Page 2                                                                                                                                         Hettle Andrews Form 2018

www.hettleandrews.co.uk