Model Policy

Use and Disposal of Oil and Fuel

A. Purpose and Scope

1. To cause or allow pollution is against the law. This procedure ensures that the use and disposal of oils and fuels is managed and maintained as required by the:

- Control of Pollution (Oil Storage) Regulations 2001

- Hazardous Waste (England and Wales) Regulations 2005 (Amendment Regulations 2016)

- Pollution Prevention and Control (Scotland) Regulations 2012

- Control of Pollution (Oil Storage) Regulations (Northern Ireland) 2010

- Guidance for Pollution Prevention (GPP) 8: Safe Storage and Disposal of Used Oils (July 2017)

- (Scotland, Northern Ireland and Wales).

B. Key Responsibilities

2. Named person or role within the contracting company is responsible for the safe storage of oil and fuels and the availability of safety equipment for relevant employees when using it.

3. Named person or role within the contracting company is responsible for ensuring all staff have been trained in the correct use of oils and fuels and related equipment and thereafter staff are responsible for their own safety when handling fuels.

C. Procedural Steps

4. Named person or role within the contracting company will complete a fuel/oil delivery form, the content of which will include:

- storage tank identifier

- ullage, (unfilled space in a container)

- quantity to be delivered

- grade of fuel to be delivered, (if applicable)

- road tanker carrying compartment quantity, (if applicable).

5. Named person or role within the contracting company will ensure the unloading of any fuel or oil is carried out in a safe manner. This includes making sure any delivery tankers are fitted with a shut off valve to be used in an emergency.

6. Any storage tanks will be monitored for the level of content prior to unloading. This will enable the operator to avoid overfilling of storage tanks.

7. The storage of oils/fuels must be in a designated area and/or in a specified and suitable storage container. Fuels, other than heating oil, are to be stored in purpose designed fuel containers, correctly labelled and stored on a spillage tray or bund sufficient to contain overspill or leakage within a secure area. Oil/fuel storage tanks/areas will be bunded and lie on impermeable surfacing to reduce the impact of a spill.

8. Named person or role within the contracting company will ensure spillage kits are available to site operatives. These will include absorbent materials. Staff will be trained as part of the spillage procedure as to when a spill kit must be used, or when the emergency services would be required.

Used spillage kit materials must be disposed of as hazardous waste. (NOTE- ‘Special’ waste in Scotland only).

9. Named person or role within the contracting company is responsible for ensuring the site plan and drainage plant, indicates where the specified fuel or oil is stored. This information will be used in the event of an emergency.

10. Named person or site operatives will ensure any oil or fuel to be disposed of will be removed from site by a licenced waste carrier, who will take the oil/fuel to a permitted facility for disposal. A Consignment Note will be completed prior to the substance leaving the site.

NOTE – see Model Policy on the Disposal of Hazardous Waste

D. Exceptions

11. Temporary staff working on-site must be supervised at all times when using machinery fuels.

# Text boxes

Insert your company logo here

Disclaimer

These example forms, checklists and Hettle Andrews policies are provided by Hettle Andrews for general guidance on matters of interest.  In making these documents available to a general and diverse audience it is not possible to anticipate the requirements or the hazards of any subscriber’s business.  Users are therefore advised to carefully evaluate the contents and adapt the forms and checklists to suit the requirements of each situation.  Hettle Andrews does not accept any liability whatsoever for injury, damage or other losses which may arise from reliance on this information and the use of these documents.

Copyright of these documents remains with Hettle Andrews and whilst subscribers are permitted to make use of them for their own purposes, permission is not granted for resale of the intellectual property to third parties.