Date: __________________	Room No. / Location: _________________
Machinery	Checks to be undertaken	Check completed	Comments	Action required	Action completed (date)	Action completed by (signature)
Disc and belt sanding machines	Clean any dust not removed by the extraction system.
	Check condition of sanding belt/disc and replace if torn/worn.
	Check fit of sanding table to disc/belt (it should be as close as possible, normally no greater than 2 mm).
	Check that quadrant guard is in the correct position.
Drilling machines	Check that the chuck guard is clean, functions correctly and is not cracked/broken.
	Make sure that the guard over the driving belt fits correctly and that the inter-lock or securing device is in place and working correctly.
Bench-mounted jig saws	Clean any dust not removed by the extraction system.
	Check condition of blade and replace if blunt.
	Check that blade guard is correctly set.
	Where fitted, check that machine ‘foot’ functions correctly.
Band saws	Clean any dust not removed by the extraction system.
	Check condition of blade; replace if blunt or if welded joint on blade is suspect.
	Check that blade guard is correctly set.
	Check that machine braking system functions correctly.
Circular saws	Clean any dust not removed by the extraction system.
	Check condition of blade and replace if blunt.
	Check that top or crown guard is correctly set and connected correctly to the extraction system, if the latter is fitted.
	Check that machine braking system functions correctly.
Planing machines for wood: overhand planer	Clean any dust/shavings not removed by the extraction system.
	Check that all guards are correctly set.
	Check that machine braking system functions correctly.
Planing machines for wood: thicknesser	Clean any dust/shavings not removed by the extraction system.
	Check that all guards are correctly set.
	Check that machine braking system functions correctly.
Planing machines for wood: combined planer / thicknesser	Clean any dust/shavings not removed by the extraction system.
	Check that all guards are correctly set.
	Check that machine braking system functions correctly.
Radial arm saws	Clean any dust not removed by the extraction system.
	Check that blade guard and side-protection guards are correctly set and function as required.
	Check that machine braking system functions correctly.
Wood-turning lathes	Clean any dust not removed by the extraction system, where fitted.
	Check functioning of electrical interlock for top guard on headstock, or mechan­ical fixing as appropriate.
	Check that foot switch or other emergency-stopping device functions correctly.
	Check that mandrel nose guard for unused spindle nose is in place.
Metal-turning lathes	Clean chuck guard and any chip screens if fitted.
	Check functioning of electrical interlock on chuck guard.
	Check that cover plate on outer end of hollow mandrel is in place.
	Check functioning of electrical interlock on change wheel guard.
Milling machines – horizontal/ / vertical	Clean all cutter guards.
	Check sharpness of milling cutters; take out of use any that are blunt or damaged.
Power hacksaws	Check condition of blade and replace if blunt, or damaged.
	Check that machine functions correctly.
Mortising machines / (pre-use check)	Check condition of chisel and auger bit; replace or sharpen if blunt or damaged.
	Check that the vice functions correctly.
	Check that all guards are in place, including the guard around the auger chuck.
	Visually check condition of electrical switches, conduit, cable, etc.
	Lubricate if necessary.

Completed By: ____________________ (Print name) ____________________ (Signature)

Disclaimer
These example forms, checklists and model policies are provided by Hettle Andrews for general guidance on matters of interest. In making these documents available to a general and diverse audience it is not possible to anticipate the requirements or the hazards of any subscriber’s business. Users are therefore advised to carefully evaluate the contents and adapt the forms and checklists to suit the requirements of each situation. Hettle Andrews does not accept any liability whatsoever for injury, damage or other loses which may arise from reliance on this information and the use of these documents.
Copyright of these documents remains with Hettle Andrews and whilst subscribers are permitted to make use of them for their own purposes, permission is not granted for resale of the intellectual property to third parties.